## Slide 1: Characterization of the GLONASS-K1+ spacecraft
Peter Steigenberger, Steffen Thoelert, André Hauschild, Oliver Montenbruck

## Slide 2: GLONASS Spacecraft
 | IIv | M | M+ | K1A | K1B | K1+ | K2
L1/L2 FDMA | x | x | x | x | x | x | x
L3 CDMA |  |  | x | x | x | x | x
L2 CDMA |  |  |  |  |  | x | x
L1 CDMA |  |  |  |  |  |  | x
Nav. Antennas | 1 | 1 | 2 | 2 | 1 | 2 | 2
Frequency Division Multiple Access
Code Division Multiple Access
FDMA:
CDMA:
Notes: OM => GNSS Handbook

## Slide 3: GLONASS K1+
SVN R807 launched in October 2022
  Slot number 25
  Frequency channel number -5
  Start of signal transmission on November 3, 2022
  L2 CDMA signal
  Suspected use of new clock (H-maser?)
Carrier-to-noise density ratio (C/N0)
  Javad TRE_3S receiver with CDMA-capable prototype firmware at Oberpfaffenhofen, Germany
  Averages of 8-day data arc
Notes: evalCN0.ipynb

## Slide 4: L2 Frequency Spectrum
L2SC
L2 Secure Service CDMA
  BOC(5,2.5)
L2OC
L2 Open Service CDMA
  BOC(1,1)
Measured with 30 m high-gain antenna in Weilheim, Germany
L2 CDMA
L2SC
L2SC
L2xC
L2 FDMA, k=-5
L2SC sidelobes
L2 CSI
Channel for Service Information
  BPSK(1)
L2SC sidelobes
BPSK: binary phase-shift keying
BOC: binary offset carrier
Notes: FDMA, FCN = -5: 1243.8125 MHz
CDMA: 1248.06 MHz
Peak at 1244 MHz

## Slide 5: Triple Carrier Combination (1)
Geometry- and ionosphere-free linear combination: L1, L2 FDMA, L3 CDMA

## Slide 6: Triple Carrier Combination (2)
TCC [cm]

## Slide 7: Triple Carrier Combination (3)
Possible explanations:
Clock hardware failure
Cross-talk of oscillators with slightly different frequencies and
Cross-coupling factor
Notes: 100 cpd = 15 min
For the maximum observed amplitude of about 20 cm, a cross-coupling factor of $\alpha\approx 0.02$ is obtained.

## Slide 8: One-way Carrier Phase Analysis (1)
H Maser
GNSS
receiver

## Slide 9: One-way Carrier Phase Analysis (2)
Consistency of L1 and L2 FDMA signals
Slight phase shift and increased amplitude of L3 CDMA
Notes: FDMA and CDMA navigation signal generation units driven by two distinct effective signals or
themselves responsible for clock interference

## Slide 10: Baseline Estimation (1)
Estimation of “baseline” between two antennas from triple carrier phase observations
Baseline: triple-frequency combination of the antenna- and frequency-specific PCOs
Main antenna array
L2 CDMA
antenna

## Slide 11: Baseline Estimation (2)
Javad TRE_3S receivers with CDMA-capable prototype firmware
  Oberpfaffenhofen, Germany
  Sydney, Australia
L1 FDMA, L2 and L3 CDMA
21 March – 3 June 2024
Notes: dX [m] dY [m] dZ [m]
Median: 0.7463 0.6812 -0.5781
Mean : 0.7453 0.6811 -0.5793
STD : 0.0099 0.0034 0.0528

## Slide 12: Summary and Conclusions
Enhanced GLONASS K1+ satellite design:
  First GLONASS satellite with L2 CDMA signal
  Dedicated L2 CDMA antenna
  New type of clock?
Pronounced periodic clock variations
  Pattern changes with time, periods between 15 min and a few days
  Reason unknown: clock hardware failure or cross-talk of two oscillators?
Single satellite of this type or further launches?
Notes: dX [m] dY [m] dZ [m]
Median: 0.7463 0.6812 -0.5781
Mean : 0.7453 0.6811 -0.5793
STD : 0.0099 0.0034 0.0528