## Slide 1
From Genesis to GNSS: What are the opportunities with VLBI transmitters on satellites?
Johannes Böhm, Helene Wolf, Lisa Kern, Urs Hugentobler
July 2, 2024
Notes: on behalf of co-authors

## Slide 2: Genesis
Mission of European Space Agency (ESA)
  Launch in 2028
    two years of operation
  Polar orbit in 6000 km altitude
  GNSS, SLR, VLBI, and DORIS

## Slide 3: Galileo
Next generation Galileo satellites G2G
  23222 km altitude at 56° inclination
  GNSS, SLR, and VLBI

## Slide 4: Opportunities with VLBI transmitters on satellites
Orbit determination in the celestial reference frame
VLBI station coordinate determination in the frame of the satellite orbit

## Slide 5: Estimation of orbital elements - Galileo
Example: Jan. 1, 2021 00:00 – 24:00
  12 station network
  GSAT0101 (E11)
Schedule with 10% satellite observations
  10 seconds on-source time
Estimation of orbital elements
  one value for 24 hours
  quasars and stations fixed
  EOP from quasar observations
Monte Carlo simulation
  tropospheric turbulence, clock variation, 10 ps white noise per observations
Notes: Tropospheric turbulence main contribution

## Slide 6: Estimation of orbital elements - Galileo
Formal errors and repeatability of orbital elements
  partials from the Bernese GNSS Software
Semi-major axis a well determinable
Argument of perigee  difficult to determine
Right ascension  directly accessible
Notes: although radial component not well determinable

## Slide 7: Estimation of orbital elements - Genesis
Under development
We expect better results for Genesis (better geometry)

## Slide 8: Estimation of VLBI station coordinates
Estimation in the frame of the satellite observed
  assessment of frame ties w.r.t. quasar frame
  additional information on local ties
Additional observations to quasars critical for troposphere parameters
Skyplot at Wettzell in 24 hours with one transmitter on Galileo and Genesis
Genesis
Galileo

## Slide 9: Estimation of VLBI station coordinates - Galileo
Station coordinate scatter from 24h sessions
  Station coordinates from satellite observations only (NNR)
  3 VLBI transmitters (VT) in plane A
  30% satellite observations
Hardly improvement with 4th VT
Scatter with one VT >3cm

## Slide 10: Estimation of VLBI station coordinates - Genesis
Station coordinate scatter from 24h sessions
  Station coordinates from Genesis observations only (NNR)
  VLBI transmitter on Genesis
  10% Genesis observations

## Slide 11: Estimation of VLBI station coordinates - Genesis
How many weeks do we need for millimeter precision?
  One 24h session per week with 12 station network
  Stacking of normal equations

## Slide 12: Estimation of VLBI station coordinates - Genesis
WETTZ13S
One year
Setup

## Slide 13: Estimation of VLBI station coordinates - Genesis

## Slide 14: Estimation of VLBI station coordinates - Genesis
Station coordinate scatter of yearly solutions
  1 to 2 mm level
  no orbit errors simulated
  observation errors 10 psec
Notes: The troposphere is in the simulation, the rest is depending on us

## Slide 15: Summary and conclusions
VLBI useful tool for orbit determination
  combination with other techniques pending
Simulations with Genesis promising
  however more realistic error scenarios required including orbit errors