## Slide 1
ESA UNCLASSIFIED – For ESA Official Use Only
GENESIS: A Multi-Technique Geodetic Observatory in Space
P.Waller, S.Gidlund, G.Fusco, E.Honoré-Livermore, E.Sakalauskaite: ESA ESTEC
E.Schoenemann, W.Enderle: ESA ESOC
V.Navarro: ESA ESAC

## Slide 2: GENESIS Mission Objectives
Index
01
GENESIS Science
Overview of
…The Mission
…The System
…The Satellite and Payloads
Scientific Setup
Conclusions
02
03
04
05

## Slide 3: GENESIS Primary Objectives
GEODESY and REFERENCE FRAMES
Contribute to improve ITRF accuracy and stability by providing in-orbit colocation and necessary combined processing for the four space-based geodetic techniques that contribute to its realization. The goal is to contribute to the achievement of the Geodetic Global Observing System (GGOS) objectives for the ITRF realisation, aiming for a parameter accuracy of 1 mm and a stability of 0.1 mm/year, in order to provide significant scientific benefits in Earth modelling, and to support a wide range of societal applications (as endorsed by the United Nation resolution A/RES/69/266).
Contribute to improve the link between the ITRF and the ICRF, thanks to the increased consistency of the Earth Orientation Parameters (EOP). In particular, this mission shall allow for the first time a link between the orbit reference frame, ITRF and ICRF.
Targets:
Accuracy: 1 mm
Stability: 0.1 mm per year

## Slide 4: GENESIS-enabled Science and Applications
Geophysics: Mantle, Oceans
Tectonic motions
Post-glacial rebound
Ice melting, Ice mass loss
Sea level change…
Geophysics: Deep Interior
Geo-centre motion
Core flows
Magnetic field…
Geodesy, Reference Frames
GNSS, Navigation
Earth Sciences
“Evolving the Geodetic Infrastructure to Meet New Scientific Needs”,
National Academies of Sciences, Engineering and Medicine (2020)
Navigation to the Moon, and beyond…
Improved GNSS POD (LEO, MEO, GEO), calibrations…
Atmospheric Physics
Iono, Plasmaspheric density
Radiation budgets, Earth Energy imbalance…
Improved ITRF, EOPs,
Unified Reference Frames

## Slide 5: Overview of the GENESIS Mission
  GENESIS is an ESA Mission, managed by the ESA Navigation Directorate and part of its Optional FutureNAV Programme.
    Italy
    Belgium
    France
    Switzerland
    United Kingdom
    Hungary
Management

## Slide 6: Overview of the GENESIS Mission
  Industrial Activities
  Single contract for Phases A/B/C/D/E
  Development and Qualification of Satellite and Ground Segment
  Launch and Early Operations (including calibrations)
  2 years of Operation (Option for extension)
  Data exploitation (making use of ESA facilities)
  4 on-board instruments:
    GNSS receiver
    VLBI transmitter
    SLR reflector
    DORIS receiver
  + Strong involvement of the Scientific Community and International Geodetic Services
Mission Scope

## Slide 7: Overview of the GENESIS Mission
Industry
Scientific
Community
ESA

## Slide 8: Overview of the GENESIS Mission
LAUNCH 2028
2 years of Operations
Option for extension
Kick Off of activities
22 April 2024
Preliminary Design Review (PDR)
Critical Design Review (CDR)
Qualification and Acceptance Review (QAR)
System Requirements Review (SRR)

## Slide 9: GENESIS System Overview
System:
Satellite
GCS (Ground Control Segment)
ESA PROAD (PROcessing, Archiving & Distribution)
Existing infrastructure (GNSS, SLR, VLBI, DORIS)
Four on-board geodetic Instruments:
SLR: passive reflector
DORIS, GNSS: on-board receivers
VLBI: on-board transmitter in existing VLBI frequency bands
Mission Phases:
Launch and commissioning
In-orbit test and calibration
Operations
End of mission
Four geodetic payloads:
VERY-LONG-BASELINE INTERFEROMETRY (VLBI) Transmitter
SATELLITE LASER RANGING (SLR) Retroreflector
GLOBAL SATELLITE NAVIGATION SYSTEMS (GNSS) Receiver (Nadir and Zenith antennas)
DORIS Receiver

## Slide 10: GENESIS Satellite and Payload Overview
GNSS
GNSS
SLR
VLBI
DORIS
GNSS
GCS
PROAD
users
Description
Satellite ~250-300kg, ~6000km alt. (MEO), ~95º inclination
Platform: maximum reuse of qualified equipment
Payload: 4 co-located geodetic instruments (GNSS, DORIS, SLR, VLBI) and an ultra-stable oscillator for synchronisation
Key drivers:
Radiation environment: total dose and single events effects
Radiofrequency and electromagnetic compatibility
Non-gravitational forces: mechanisms, geometry, materials...
Spacecraft centre-of-mass and attitude law
Synchronisation of active instruments to the on-board oscillator
On-board instruments systematic biases and their calibrations: phase centres + group delays

## Slide 11: GENESIS Payload: GNSS Receiver
Description:
Multi-channel/multi-GNSS receiver
Nadir and Zenith antennas
Externally synchronised to on-board reference frequency
Key drivers:
Quality of observables (signal-to-noise ratio, Cycle Ambiguity Resolution, ...)
GNSS visibility at 6000km
Antenna Phase Center Offsets calibration (vs. azimuth/elevation, vs. temperature)
Antenna location on platform
Instrument and antenna group-delay stability
On-board time tagging of observables

## Slide 12: GENESIS Payload: VLBI Transmitter
Description:
4 frequency bands within [2GHz, 14GHz]
PSFD: [0.5Jy, 10Jy]
Single nadir antenna with full Earth Field of View
Externally synchronised to on-board reference frequency
Key drivers:
ITU regulations, RF Interferences and EMC
Multi-band antenna over wide bandwidth
Compatibility with both legacy and VGOS stations
Antenna PCOs calibration (vs. azimuth/elevation, vs. temperature)
Instrument group-delay calibration
VLBI Radio Telescope in Wettzell, Germany
(https://shorturl.at/ctwGP)
VLBI Transmitter breadboard for G2G
(https://h2020nav.esa.int/project/h2020-038-01)

## Slide 13: GENESIS Payload: Laser Retro-reflector
Description:
Passive LRR on the nadir-side of the satellite
Array of corner cube reflectors
Key drivers:
Field of view and optical cross-section at 6000km
Thermo-elastic effects, materials...
Accommodation
Compatibility with SLR stations
PCO calibration

## Slide 14: GENESIS Payload: DORIS receiver
Description:
Doppler tracking of UHF and S-band ground beacons
Dual-frequency nadir antenna
Externally synchronised to on-board reference frequency
Key drivers:
Ground Beacon visibility at 6000km
Quality of observables and on-board processing
Antenna PCOs calibration (vs. azimuth/elevation, vs. temperature)
Instrument group-delay calibration
MEO radiation environment

## Slide 15: GENESIS Data PROcessing, Archiving and Delivery
International Geodetic Services
SLR (ILRS)
VLBI (IVS)
GNSS (IGS)
GENESIS POD Products and other Data
GNSS+Doris Measurements
Navigation Support Office
Industry
GNSS Measurements + Additional Data
ESAC GNSS Science Support Center
GENESIS Data and Products Dissemination
CNES
Doris Measurements
PROAD
GNSS
Galileo & GPS
DORIS

## Slide 16: GENESIS Science Team
GENESIS Science Team
GENESIS Science Management Board
GENESIS Science Exploitation Team (GSET)
ESA GENESIS Scientific Representative
GENESIS Mission Lead Scientific Coordinator
GENESIS Mission Lead Scientific Co-Coordinator
Working Groups Chairs
GENESIS Mission Lead Scientific Coordinator and Co-Coordinator
GENESIS Working Groups (WGs)
  WG1: ITRF and Combination of Techniques
  WG2: GNSS
  WG3: VLBI
  WG4: DORIS
  WG5: Laser Ranging

## Slide 17: GENESIS Science Workshop
29th February @ ESOC
Agenda
Morning
Over 100 people onsite and online
Attendance from all relevant International Geodetical Services (Chairs or deputies):
Presentations from the ESA GENESIS project team
Interactive working group discussions
Wrap up and Conclusions
IAG, IERS, IGS, IVS, ILRS, IDS
Strong commitment and engagement from the community
Afternoon
“GENESIS – A Mission for the World”

## Slide 18: GENESIS Science Exploitation Team - Nominations
Coordinator
Co-Coordinator
WG1: ITRF & Combination of Techniques
WG3: VLBI
WG4: DORIS
Zuheir Altamimi Institut national de l'information géographique et forestière – IGN
Florian Seitz Deutsches Geodätisches Forschungsinstitut-Technischen Universität München – DGFI
WG2: GNSS
Rolf Dach Universität Bern
Benjamin Männel Deutsches GeoForschungsZentrum – GFZ
Rüdiger Haas Chalmers Tekniska Högskola
Guilhem Moreaux CLS-Collecte Localisation Satellites
WG5: Laser Ranging
Clément Courde Centre national de la recherche scientifique-Géoazur
Francesco Vespe ASI Space Geodesy Centre at Matera
Özgur Karatekin Royal Observatory of Belgium – RoB

## Slide 19
ESA UNCLASSIFIED – For ESA Official Use Only
Thanks to combined efforts from Scientific Community, ESA Member States, Industry and ESA, the GENESIS Mission has become a reality!
This challenging mission will be a stepping stone towards improved GNSS and navigation, together with addressing major scientific and societal goals
Despite a challenging schedule, ESA, Industry and the Scientific community are fully committed to the success of the Mission, starting with a System Requirement Review in fall 2024
We are looking forward to updating the community on the progress of the mission
GENESIS – AT THE FOUNDATION OF NAVIGATION
To conclude…

## Slide 20
ESA UNCLASSIFIED – For ESA Official Use Only
Thank you for your attention