## Slide 1
ESA UNCLASSIFIED – For ESA Official Use Only
GENESIS – PROAD
Data PROcessing, Archiving and Delivery
W. Enderle1, F. Dilssner2, T. Springer2, M. Otten2, S. Bruni2, M. van Kints3, F. Gini1, E. Schoenemann1
1ESA/ESOC - Navigation Support Office; 2PosiTim@ESA/ESOC - Navigation Support Office; 3VisionSpace@ESA/ESOC - Navigation Support Office
V. Navarro: ESA ESAC

## Slide 2: GENESIS – PROAD General Interface Overview
PROAD
GENESIS Satellite
On-Board Measurements
- GNSS (GAL/GPS)
- DORIS
Industry
- GENESIS Satellite
- Design and Development
- Operations
ESA
- Project
- PROAD
Precise Orbit Determination
Data Archive and I/F for Data Dissemination
International Geodetic Community
- IERS and four geodetic Services
- International Geodetic Oerganisations
Ground Support Infrastructure
- SLR Network
- VLBI Network
- IGS Network
International Community
- Geodetic Community
- Science Community
CNES DORIS

## Slide 3: GENESIS – PROAD Data Flow
GNSS
Galileo & GPS
DORIS
International Geodetic Services
SLR (ILRS)
VLBI (IVS)
GNSS (IGS)
GENESIS POD Products and other Data
GNSS+Doris Measurements
Navigation Support Office
Industry
GNSS Measurements + Additional Data
ESAC GNSS Science Support Center
GENESIS Data and Products Dissemination
CNES
Doris Measurements
PROAD

## Slide 4: GENESIS – PROAD Precise Orbit Determination Data Products
Products generated by PROAD
Precise Orbit Determination for Galileo and GPS satellites
Precise Orbit Determination for GENESIS satellite
In-Orbit validation of the pre-launch calibrated space ties between the different geodetic payloads on board the GENESIS satellite
Additional Products are possible, based on agreements with International Organizations

## Slide 5: GENESIS – PROAD Precise Orbit Determination Data Products
Potential New PROAD Products
Combined solutions
  Solution A: coherent processing of all four geodetic techniques in a single least squares process
  Solution B: Solution A including MEO satellites
  Solution C: Solution B including LEO satellites (e.g. Sentinel satellites, Lageos satellites, etc. )
    Important: so far, no GNSS LEO contribution towards the ITRF

## Slide 6: GENESIS – Contributions from ESA’s Navigation Support Office
In addition to the PROAD activities, ESA’s Navigation Office will also contribute to the generation of the ITRF by provision of individual solutions for all four geodetic techniques as official Analysis Center (AC) to IERS.

## Slide 7: GENESIS – PROAD Collaborating across ESA
PROcessing, Archiving and Distribution (PROAD)
ESAC
ESOC
Data Processing
&
Precise Orbit Determination
Data Storage
&
Distribution
Data and Products
Measurements and Ancillary Data
POD Products and Additional Data
Navigation Support Office
GNSS Science Support Centre
VLBI
SLR
GNSS

## Slide 8: GENESIS – PROAD Advanced Ingestion Services
UPLOAD
DOWNLOAD
Contributors
GSSC
REPOSITORY
METADATA
Pull
Push
ESAC
…

## Slide 9: GENESIS – PROAD
The success of GENESIS depend on international cooperation.
Thank you for your support!